## Slide 1: Fault-tolerant streaming with FEC via Capillary-routing
International Conference on Communications, Circuits And Systems – ICCCAS’06 – Bravo Hotel, Gui Lin, China - Monday, June 26, 2006
by Emin Gabrielyan,
Switzernet.com (VoIP) and
Swiss Federal Institute of Technology (EPFL)
Switzerland
Switzernet
Notes: Hello everybody. My name is Emin Gabrielyan and my talk is about multi-path routing solutions for real-time streaming applications using Forward Error Corrections. This is a joint work between Swiss Federal Institute of Technology (EPFL) and Switzernet, a VoIP company in Switzerland

## Slide 2: Structure of my talk
The advantages of packet level Forward Error Correction (FEC) in Off-line streaming
Difficulties arising in application of packet level FEC in Real-time streaming
How the difficulties of application of FEC in real-time streaming are solved by multi-path routing
Generating multi-path routing patterns of various path diversity
Relation between the diversity factor and the advantageousness of the routing (for real-time streaming)
Notes: First I will talk about the advantages of the packet level FEC codes (Forward Error Correction codes) in off-line streaming. Then I’ll present the difficulties arising in real-time streaming. I’ll show how multi-path routing solves these difficulties of real-time streaming. I’ll present an algorithm for building different multi-path routing patterns of increasing diversity. Finally I’ll present the relation between the diversity strength of the multi-path routing and the advantageousness of the routing for real-time streaming.

## Slide 3: Off-line streaming of a file using Digital Fountain FEC
A file can be chopped into equally sized source packets
Digital fountain code can unlimitedly generate different checksum packets
…
…
…
…
…
Notes: In off-line streaming a file can be divided into a given number of packets and a digital fountain code can generate an infinite number of checksum packets

## Slide 4: Decoding of a file encoded by Digital Fountain Codes
It is sufficient to collect a fixed number of checksum packets and the file can be recovered
Choice of packets is not important only the number of packets matters
As if with water fountain: you need to fill your cup by collecting a sufficient quantity of any drops
…
…
…
Notes: These checksum packets have a very interesting property. It is sufficient to collect a given number of those packets in order to be able to recover the original file (using a decoding algorithm). It does not matter which particular checksum packets are collected, only their quantity matters. Like with a water fountain, you need to feel your cup and you do not care about the choice of the drops.

## Slide 5: An application: Delivery of large files over satellite link
For example delivery of recurrent update of GPS maps to thousands of vehicles
  There is no feedback channels
  Continuous reception may require a constant visibility of 24 hours or more
Notes: Delivery of large files over satellite link is a good example for off-line streaming. There is no feedback channel. A large file – for example an update of GPS maps – must be delivered to motor vehicles through a satellite link. Car does not have transmission possibilities in order to provide a feedback channel. Moreover a file is so large that that a continuous visibility of 24 hours or more is required for the continuous delivery.

## Slide 6: Arbitrary network losses
The visibility of a car is however fragmental and is arbitrary due to:
Tunnels
Whether conditions
Underground parking, etc
Notes: That is a condition which cannot be satisfied in real world. The car’s visibility will be interrupted by tunnels, underground parking, or many other reasons. It seems that the task does not have a solution, but …

## Slide 7: Raptor (digital fountain) code in satellite one-way transmissions
Solution is broadcasting with digital fountain code
If reception is interrupted the missing packets are collected later
Raptor code is also a new standard for MBMS in 3G mobile networks
Notes: The satellite can transmit continuously different checksum packets of the original file encoded on-the-fly according to a digital fountain code. Now interruptions are not important. Only a sufficient quantity of any of the checksum packets is required to collect. If reception is interrupted the missing quantity can be collected later. A satellite can keep generating and transmitting the checksum packets during a long period of time (let’s say during 10 days) and with a high probability a car can collect the sufficient number of packets to decode the original file. Not only one car, but hundreds of thousands of independent cars can simultaneously receive a large file. Honda is planning to integrate Raptor codes into digital radio in order to broadcast to its vehicles large files, such as updates of GPS maps.

## Slide 8: Unrestricted buffering time at the receiver
Reliability of off-line applications can be significantly improved with FEC codes
The benefit of off-line applications from FEC codes is spectacular
This befit relies on time diversity
There is no need of real-time delivery of information to the end user
Notes: The benefit from application of FEC in off-line streaming is spectacular. FEC significantly improves the reliability of off-line applications. This benefit relies on the fact that there is no need to deliver the information content to the end user in restricted time. In other words, off-line streaming with FEC relies on time diversity…

## Slide 9: Time diversity
If packets for information recovery are not collected at the present period of time…
The missing quantity can be collected later
Later…
And later…
Notes: If packets needed for information recovery are lost, new packets can be recollected later. If there is a new interruption later, some other packets received in future can replace the missing ones.

## Slide 10: Real-time streaming
While in off-line streaming the data can be hold in the receiver buffer …
In real-time streaming the receiver is not permitted to keep data too long in the playback buffer
Notes: However, in real-time streaming, the receiver is not permitted to hold information in its buffer too long. The information must be delivered to the user in time. For example in VoIP the round trip time cannot exceed 600 milliseconds.

## Slide 11: Long failures on a single path route
If the failures are short and fine-grained, by transmitting a large number of FEC packets, receiver may constantly have in time a sufficient number of checksum packets
If the failure lasts longer than the playback buffering limit, no FEC can protect the real-time communication
Notes: In real-time streaming, in case of losses, the checksum packets for recovering the losses must arrive quickly, before expiration of the buffering time limit at the receiver (playback buffer time). A large amount of transmitted FEC packets may constantly provide in time a sufficient number of checksum packets at the receiver. However, if a total failure last longer the permitted playback buffer time, even infinite amount of FEC checksum packets cannot deliver the information in time. FEC can be useful only if the failures last no longer than the buffering time limit at the receiver.

## Slide 12: Applicability of FEC in Real-Time streaming
Reliable Off-line streaming
Reliable real-Time streaming
Time diversity
Playback buffer limit
Real-time streaming
In off-line streaming losses can be compensated by other packets received later
In real-time streaming losses can be compensated by other packets received via another path
Path diversity is an orthogonal method making FEC applicable also for real-time streaming
Path diversity
Notes: However, if in off-line streaming the lost packets can be compensated by other packets received at another period of time, in real-time streaming they can be compensated by other packets received at the same period of time but through another communication path. Therefore the path-diversity – a method orthogonal to time diversity – can make FEC applicable also for real-time streaming.

## Slide 13: Only multi-path patterns
Intuitively we imagine the path diversity ax as shown:
It is clear that compared with single path routing any multi path routing is good
High diversity decreases the impact of individual link failures, but uses much more links, increasing the overall failure probability
Which level of path diversity is the optimal and requires the minimal encoding efforts of the sender
We must study many multi-path routings patterns of different diversity (without single path routing) in order to answer this question
Single path routing
Multi-path routing
Multi-path routing
Multi-path routing
Path diversity
Notes: Intuitively the path diversity ax must look like this. It is clear that for real-time streaming any multi-path routing is better than the single path routing. However, within multi-path routing solutions, we do not know if additional increase of diversity is beneficiary or not. Is not it sufficient for example to have only double path routing? Higher diversity minimizes the impact of individual link failures but from another side it requires a larger number of links to be used. Considering that each link has a failure probability, by using more links the overall rate of possible failures influencing the communication increases. Strong diversity may increase the FEC encoding effort of the sender, instead of decreasing. To address this question, we must study numerous multi-path routing patterns of increasing path diversity. The single path routing can be removed from our study.

## Slide 14: Capillary routing
As a method for obtaining multi-path routing patterns of various path diversity we relay on capillary routing algorithm
For any given network and pair of nodes it produces layer by layer routing patterns of increasing path diversity
Path diversity
= Layer of Capillary Routing
Notes: In order to generate different routing patterns of increasing path diversity we use an algorithm – called capillary routing algorithm. For a given source and destination this algorithm can propose various multi-path routing patterns of increasing path diversity.

## Slide 15: Capillary routing - introduction
Capillary routing first offers a simple multi-path routing pattern
At each successive layer it recursively spreads out the individual sub-flows of the previous layer
Therefore the path diversity develops as the layer number increases
Notes: Capillary routing is constructed layer by layer, suggesting at each layer a multi-path routing solution. As the layer number increases the diversity of the multi-path routing is also increasing.

## Slide 16: Capillary routing – first layer
Reduce the maximal load of all links
The construction relies on an iterative LP process
First take the shortest path flow and minimize the maximum load of all links
This will split the flow over a few main parallel routes
Notes: We use a linear programming (LP) method for constructing the capillary routing. At the first layer the objective of the linear program is to minimize the maximal load of all links. The solution of such a program distributes the flow across a few parallel paths.

## Slide 17: Capillary routing – second layer
At the second layer identify the bottleneck links of the first layer
Then minimize the flow of all remaining links, except the bottleneck links of the first layer
Reduce the load of the remaining links
Notes: At the second layer we identify the bottleneck links of the multi-path route found in the first layer. The with a new objective we minimize the maximal load of all links, except the bottleneck links of the first layer. This leads us to a additional spreading of the route, whenever it was possible.

## Slide 18: Capillary routing – algorithm
Identify the bottlenecks of the second layer
…and at the third layer reduce the maximal load of all remaining links, except the bottlenecks of the first and second layers
Repeat this iteration until all links of the communication path are enclosed in bottlenecks of the constructed layers
Notes: The third layer is constructed similarly. We identify the bottleneck links of the second layer and with an LP (Linear Programming) objective we minimize the maximal load of all links except the bottleneck links of the first and the second layers. Third layer leads to even spreader routing. We repeat this procedure until the full communication footprint of the capillary routing is discovered.

## Slide 19: Network samples
The network samples for applying capillary routing are obtained from a random walk MANET
Nodes are moving in a rectangular area
If the nodes are sufficiently close and are within the range of the coverage there is a link between the nodes [diagram]
Notes: Numerous network samples are obtained from MANET (Mobile Ad-hoc Network). Nodes are moving according a random walk algorithm. If they are sufficiently close there is a link between them. Each time frame gives us a network sample. Thus we can generate hundreds of network samples.

## Slide 20: Capillary routing examples
Here is an example of capillary routing on a small random walk ad-hoc network with 9 nodes [diagram]
An example of capillary routing on a larger network with 130 nodes [diagram]
Notes: The animation shows four multi-path routing suggestions for each time frame of a small random-walk ad-hoc network (with 9 nodes). The second animation shows four capillary routing layers on a larger network with 130 nodes.
(Press Ctrl-W to exit the animation)

## Slide 21: Weak static and strong dynamic FEC
We have now hundreds of network samples
For each network sample we have a dozen of multi-path routing suggestions of different path diversity
To evaluate these multi-path routing pattern for real-time streaming we assume a real-time application, where
  The sender uses a small constant amount of FEC checksum packets to combat weak losses and
  The sender can dynamically increase the number of FEC packets in case of serious failures
Notes: We now can create several multi-path routing suggestions for each of hundreds of network samples. In order to evaluate the efficiency of path diversity for real-time streaming, we rely on a application which streams the communication flow with a constant amount of FEC checksum packets in order to recover weak losses. In case of serious losses, the sender is capable to dynamically increase the number of redundant checksum packets.

## Slide 22: Weak FEC codes
If we need the real-time streaming to constantly tolerate a given weak packet loss rate t
We can compute accordingly the needed FEC block length = FECt
We assume Reed-Solomon code
source packets
redundant packets
FEC block
Notes: With such a model we can compute how much of FEC checksum packets (or in other words redundant packets) must be injected by the sender into the stream of original packets in order to tolerate a desired packet loss rate t. For example in order to tolerate 10% packet losses the sender may need to add 20% redundant packets. This relation can be computed taking into account the type of the used code.

## Slide 23: Strong FEC codes
Packet Loss Rate = 3%
Packet Loss Rate = 30%
When the packet loss rate observed at the receiver is below the tolerable limit t (let’s say it is 5%) the sender transmits at its usual rate
But when the packet loss rate exceeds the tolerable limit, the sender adaptively increases the FEC block size by adding more redundant packets
Notes: When the packet loss rate reported by receiver is below the tolerable limit, the sender continues transmitting at the default mode. When the packet loss rate exceeds the tolerable limit, the sender computes how much redundant packets is necessary to combat the new losses and streams the media with the required number of redundant packets.

## Slide 24: Overall number of redundant packets
Assume a uniform probability of link failures in the network
Depending on the choice of the multi-path routing between the source and destination, the sender may be required to transmit more or less redundant packets
Heavily loaded links may cause serious losses requiring significant amount of FEC packets from the sender
Many lightly loaded links increase the overall failure rate and also may require in total a large number of FEC packets to be transmitted during the communication time
Notes: Assume an equal uniform probability of link failures in the network. Depending on the topology of the multi-path routing pattern to the destination, the sender may need to transmit more or less redundant packets during the communication time. If there are heavily loaded links in the path, their failures during the communication will result to serious losses and will require a significant amount of redundant packets from the sender. If there are many links in the path, although even if they may not carry each a significant amount of traffic, the large number of such links will cause a high frequency of overall failures and may require as a result a large overall number of redundant packets to be sent by the sender during the whole communication time.

## Slide 25: Redundancy Overall Requirement
The overall amount of dynamically transmitted redundant packets during the whole communication time is proportional:
to the duration of communication and the usual transmission rate
to a single link failure frequency and its average duration
and to a coefficient characterizing the given multi-path routing pattern
Notes: The overall number of redundant packets that the sender will need to transmit during the communication time is proportional (1) to the duration of the communication, (2) to the estimated frequency and duration of single link failures and (3) to a coefficient depending only on the chosen multi-path routing. Smaller this coefficient, better the multi-path routing is.

## Slide 26: Equation for ROR
This routing coefficient is computed according the above equation, where
FECr(l) is the FEC transmission block size in case of the complete failure of link l, which is a function of the load of the link under the given routing pattern
FECt is the FEC block size at default streaming (tolerating loss rate t)
Notes: This routing coefficient, depending only on the topology of the multi-path routing, is computed according to this equation. We call it ROR which stands for Redundancy Overall Requirement. Please refer to the paper for more details.

## Slide 27: ROR coefficient
Smaller the ROR coefficient of the multi-path routing pattern, better is the choice of multi-path routing for real-time streaming
By measuring ROR coefficient of multi-path routing patterns of different path diversity, we can evaluate the advantages (or disadvantages) of diversification
Multi-path routing patterns of different diversity are created by capillary routing algorithm
Notes: Smaller the ROR coefficient of the multi-path routing pattern, better is the choice of multi-path routing for real-time streaming. By computing ROR coefficients of multi-path routing suggestions of various path diversity we can evaluate the advantageousness of increase of the diversity. For choices of multi-path routing we use the capillary routing layers, where the layer indicates how strong is the path diversity.

## Slide 28: ROR as a function of diversity
0
5
10
15
20
25
30
35
40
45
50
55
60
layer1
layer2
layer3
layer4
layer5
layer6
layer7
layer8
layer9
layer10
capillarization
Average ROR rating
Here is ROR as a function of the capillarization level
It is an average function over 25 different network samples (obtained from MANET)
The constant tolerance of the streaming is 5.1%
Here is ROR function for a stream with a static tolerance of 4.5%
Here are ROR functions for static tolerances from 3.3% to 7.5%
3.3%
3.9%
4.5%
5.1%
7.5%
6.3%
Notes: Here is ROR coefficient as a function of the capillary routing layer. We see that the capillarization of up to the 10th layer is advantageose as the ROR coefficient of the routing continues to decrease. The 5.1% at the side of the curve indicates the default constant tolerance of the streaming to the losses. The next example (the second curve) is for the streaming with the default static tolerance to 4.5% of packet losses. The curve is different, but the path diversity is beneficiary as well. Examples with other streaming parameters (all the remaining curves) show that even the strong path diversity with many underlying links always remains beneficiary.

## Slide 29: ROR rating over 200 network samples
ROR function of the routing’s capillarization computed on several sets of network samples
Each set contains 25 network samples
Network samples are obtained from random walk MANET
Almost in all cases path diversity obtained by capillary routing algorithm reduces the overall amount of FEC packets
Notes: Here is an example for many other network samples. This chart represents average curves for 200 network samples. It shows that the path diversity in typical network conditions is beneficiary. It is not only important the conversion of a single path routing to a simple multi-path routing. We show that in real-time streaming, with an additional development of the path diversity we may achieve a new significant gain in the number of redundant packets that the sender needs to transmit for protecting the communication.

## Slide 30: Conclusions
Except a few pathological cases in typical network environment strong path diversity is beneficiary for real-time streaming
Capillary routing patterns significantly reduce the overall number of redundant packets required from the sender
Today’s commercial real-time streaming applications do not rely on packet level FEC, since with single path routing FEC is helpless
With multi-path routing patterns real-time applications can have great advantages from application of FEC
When the underlying routing cannot be changed, for example in public Internet, rely computers of an overly network can be used to achieve a multi-path communication flow
Notes: Except a few pathological cases in typical network environment strong path diversity is beneficiary for real-time streaming. Capillary routing patterns significantly reduce the overall number of redundant packets required from the sender. Today’s commercial real-time streaming applications do not rely on packet level FEC, since with single path routing FEC is helpless. With multi-path routing patterns real-time applications can have great advantages from application of FEC. When the underlying routing cannot be changed, for example in public Internet, rely computers of an overly network can be used to achieve a multi-path communication flow. This is the end of my talk.

## Slide 31: Questions ?
Thank you !
Questions ?
emin.gabrielyan@switzernet.com
or
emin.gabrielyan@epfl.ch
Notes: Thank you for your attention.