## Slide 1: Rating of Routing by Redundancy Overall Need
6th International Conference on ITS Telecommunications (ITST06, pp. 786-789)
by Emin Gabrielyan
Thursday, June 22, 2006
Switzernet.com (VoIP) and
Swiss Federal Institute of Technology (EPFL)
Switzerland
Switzernet

## Slide 2: Rating of Multi-Path Routing for Fault-Tolerant Real-Time Streaming with FEC
Emin Gabrielyan
Switzernet Sàrl and EPFL
emin.gabrielyan@switzernet.com
emin.gabrielyan@epfl.ch

## Slide 3: Structure of my talk
The advantages of packet level Forward Error Correction (FEC) in Off-line streaming
Difficulties arising in application of packet level FEC in Real-time streaming
Proposed solutions

## Slide 4: Off-line streaming of a file on the example of Digital Fountain Codes
A file can be chopped into equally sized source packets
Digital fountain code can generate an unlimited number of different checksum packets
…
…
…
…
…

## Slide 5: Digital Fountain Codes
It is sufficient to collect almost as many checksum packets as there were source packets – and the file can be recovered
Like with a water fountain: you need to fill your cup by collecting a sufficient quantity of drops – no matter which drops
…
…
…

## Slide 6: An application of the digital fountain code: Large file delivery over satellite link
For example delivery of recurrent update of GPS maps to thousands of vehicles
  There is no feedback channels
  Reception may require continuous visibility of 24 hours or more

## Slide 7: Arbitrary visibility pattern
However the visibility of a car is fragmental and is arbitrary due to:
Tunnels
Whether conditions
Underground parking, etc

## Slide 8: Raptor (digital fountain) code in satellite transmission
Solution: broadcasting with digital fountain code
If reception is interrupted the missing packets are collected later
Raptor code is also a new standard for MBMS in 3G mobile networks

## Slide 9: Unrestricted buffering time at the receiver
The benefit of off-line applications from FEC codes is spectacular, because:
  There is no need of immediate real-time delivery of information to the end user
The reliability of Off-line streaming with FEC relies on Time Diversity:

## Slide 10: Time diversity
If packets for information recovery are not collected at the present period of time…
The missing quantity can be collected later
Later…
And later…

## Slide 11: Real-time streaming
In off-line streaming the data can be hold in the receiver buffer
But in real-time streaming the receiver is not permitted to keep data too long in the playback buffer

## Slide 12: Long failures on a single path route
Playback buffer
If the failures are transient and fragmental FEC can be useful
If the failure lasts longer than the playback buffering time of the receiver, no FEC can protect the real-time communication
Failure time

## Slide 13: Real-time streaming – time diversity?
Time diversity: that was the keystone for application of FEC in off-line streaming
Is useless for real-time streaming

## Slide 14: Applicability of FEC in Real-Time streaming
Reliable Off-line streaming
Reliable real-Time streaming
Time diversity
Playback buffer limit
Real-time streaming
Packet loss can be compensated by other packets received later (buffering time scale)
But the losses can be also compensated by other packets received at the same time, but via another path (path diversity scale)
Path diversity is an orthogonal ax making FEC applicable for real-time streaming without needing long buffering
Path diversity

## Slide 15: Path diversity ax
Intuitively we imagine the path diversity ax as shown:
Single path routing
Multi-path routing
Multi-path routing
Multi-path routing
zero
Path diversity

## Slide 16: Which is the best diversity?
It is clear that compared with single path routing all levels of diversity are good
From another side many alternative paths increase the number of underlying links and the potential rate of failures in the communication path
Which is the optimal level of path diversity?

## Slide 17: Only multi-path patterns
The single path routing does not interest us and we remove it from this study
Single path routing
Multi-path routing
Multi-path routing
Multi-path routing
zero
Path diversity

## Slide 18: Capillary routing
As a method for obtaining multi-path routing patterns of various path diversity we relay on capillary routing algorithm
For any given network and pair of nodes it produces layer by layer routing patterns of increasing path diversity
Path diversity
= Layer of Capillary Routing

## Slide 19: Capillary routing - introduction
Capillary routing is constructed layer by layer
First it offers a simple multi-path routing pattern
At each successive layer it recursively spreads out the individual sub-flows of the previous layer
Therefore the path diversity develops as the layer number increases

## Slide 20: Capillary routing – first layer
Reduce the maximal load of all links
Capillary routing is constructed by an iterative LP process
First take the shortest path flow and minimize the maximum load of all links
This will split the flow over a few main parallel routes

## Slide 21: Capillary routing – second layer
At the second layer identify the bottleneck links of the first layer
These are the links whose load cannot be further reduced
Then minimize the flow of all remaining links, except the bottleneck links of the first layer
Reduce the load of the remaining links

## Slide 22: Capillary routing – algorithm
Identify the bottlenecks of the second layer
…and at the third layer reduce the maximal load of all remaining links, except the bottlenecks of the first and second layers
Repeat this iteration until all links of the communication path are enclosed in bottlenecks of the constructed layers

## Slide 23: Network samples
The network samples for applying capillary routing are obtained from a random walk MANET
Nodes are moving in a rectangular area
If the nodes are sufficiently close and are within the range of the coverage there is a link between the nodes [diagram]

## Slide 24: Capillary routing examples
Here is an example of capillary routing on a small random walk ad-hoc network with 9 nodes [diagram]
An example of capillary routing on a larger network with 130 nodes [diagram]

## Slide 25: Weak static and strong dynamic FEC
To evaluate a multi-path routing pattern for real-time streaming we assume an application model, where the sender:
Uses a small static amount of FEC codes to combat weak losses and
Dynamically added FEC packets to combat strong failures

## Slide 26: Constant weak FEC codes
We assume an application streaming the media with a little constant static number of FEC packets for combating weak failures
Such that the real-time streaming constantly tolerates weak packet loss rate 0<t<1
We assume Reed-Solomon code
And compute accordingly the needed FEC block length = FECt
source packets
redundant packets
FEC block

## Slide 27: Strong dynamic FEC codes
Packet Loss Rate = 3%
Packet Loss Rate = 30%
When the packet loss rate observed at the receiver below the tolerable limit t (let’s say 5%) the sender transmits at its usual rate
But when the packet loss rate exceeds the tolerable limit, the sender increases the FEC block size by adding more redundant packets

## Slide 28: Overall number of redundant packets
Assume a uniform probability of frequency of link failures
Bigger the number of underlying links higher the total rate of link failures (shall we use shortest path routing then?)
But we also must try to minimize the number of highly loaded links

## Slide 29: Redundancy Overall Requirement
The overall amount of dynamically added extra FEC packets during communication time is proportional:
to the usual packet transmission rate of the sender
to the duration of communication
to the single link failure rate
to the single link failure time
and to a coefficient characterizing the given multi-path routing pattern

## Slide 30: ROR - equation
This routing coefficient is computed according the above equation, where
FECr(l) is the FEC transmission block size in case of the complete failure of link l
FECt is the default streaming FEC block size (tolerating weak failures)

## Slide 31: ROR coefficient
Smaller the ROR coefficient of the multi-path routing pattern, better is the choice of multi-path routing for real-time streaming
For a given pair of nodes, by measuring the ROR coefficient of different layers of the capillary routing – we can evaluate the benefits from the capillarization

## Slide 32: ROR as a function of capilarization
0
5
10
15
20
25
30
35
40
45
50
55
60
layer1
layer2
layer3
layer4
layer5
layer6
layer7
layer8
layer9
layer10
capillarization
Average ROR rating
Here is ROR as a function of the capillarization level
It is an average function over 25 different network samples (obtained from MANET)
The constant tolerance of the streaming is 5.1%
Here is ROR function for a stream with a static tolerance of 4.5%
Here are ROR functions for static tolerances from 3.3% to 7.5%
3.3%
3.9%
4.5%
5.1%
7.5%
6.3%

## Slide 33: ROR rating over 200 network samples
ROR function of the routing’s capillarization computed on several sets of network samples
Each set contains 25 network samples
Network samples are obtained from random walk MANET
Almost in all cases path diversity obtained by capillary routing algorithm reduces the overall amount of FEC packets

## Slide 34: Conclusions (1 of 2)
Commercial real-time streaming applications do not relay on packet level FEC, since even heavy FEC cannot protect communication against a long failure on a single path
By studying a wide range of routing topologies we have shown that a proper choice of multi-path routing can make FEC extremely efficient
We introduced capillary routing algorithm offering steadily diversifying patterns
We introduce ROR – a method for rating a routing pattern by a single scalar value

## Slide 35: Conclusions (2 of 2)
In general: the path diversity increases the communication footprint and the overall failure rate of the underlying links
It may also increase the overall number of FEC packets required for protection of communication
However the routing patterns built by capillary routing algorithm decrease substantially the overall amount of required FEC packets

## Slide 36: Thank you !
Questions ?