## Slide 1: Three Topics in Parallel Communications
Public PhD Thesis presentation by Emin Gabrielyan

## Slide 2: Parallel communications: bandwidth enhancement or fault-tolerance?
1854 Cyrus Field started the project of the first transatlantic cable
After four years and four failed expeditions the project was abandoned

## Slide 3: Parallel communications: bandwidth enhancement or fault-tolerance?
12 years later
Cyrus Field made a new cable (2730 nau. miles)
Jul 13, 1866: laying started
Jul 27, 1866: the first transatlantic cable between two continents was operating

## Slide 4: Parallel communications: bandwidth enhancement or fault-tolerance?
The dream of Cirus Field was realized
But the he immediately send the Great Eastern back to sea to lay the second cable

## Slide 5: Parallel communications: bandwidth enhancement or fault-tolerance?
September 17, 1866 – two parallel circuits were sending messages across the Atlantic
The transatlantic telegraph circuits operated nearly 100 years

## Slide 6: Parallel communications: bandwidth enhancement or fault-tolerance?
The transatlantic telegraph circuits were still in operation when:
In March 1964 (in a middle of the cold war): Paul Baran presented to US Air Force a project of a survivable communication network
Paul Baran

## Slide 7: Parallel communications: bandwidth enhancement or fault-tolerance?
According to the theory of Baran
Even a moderated number of parallel circuits permits withstanding extremely heavy nuclear attacks

## Slide 8: Parallel communications: bandwidth enhancement or fault-tolerance?
Four years later, October 1, 1969
ARPANET, US DoD, the forerunner of today’s Internet

## Slide 9: Bandwidth enhancement by parallelizing the sources and sinks
Bandwidth enhancement can be achieved by adding parallel paths
But a greater capacity enhancement is achieved if we can replace the senders and destinations with parallel sources and sinks
This is possible in parallel I/O (first topic of the thesis)

## Slide 10: Parallel transmissions in low latency networks
In coarse-grained HPC networks uncoordinated parallel transmissions cause congestion
The overall throughput degrades due to conflicts between large indivisible messages
Coordination of parallel transmissions is presented in the second part of my thesis

## Slide 11: Classical backup parallel circuits for fault-tolerance
Typically the redundant resource remains idle
As soon as there is a failure with the primary resource
The backup resource replaces the primary one

## Slide 12: Parallelism in living organisms
A bio-inspired solution is:
To use the parallel resources simultaneously
Renal artery
Renal artery
Renal vein
Renal vein
Ureter
Ureter

## Slide 13: Simultaneous parallelism for fault-tolerance in fine-grained networks
All available paths are used simultaneously for achieving the fault-tolerance
We use coding techniques
In the third part of my presentation (capillary routing)

## Slide 14: Fine Granularity Parallel I/O for Cluster Computers
SFIO, a Striped File parallel I/O
Notes: In this part of my talk I’m going to present a Parallel I/O solution for cluster computers

## Slide 15: Why is parallel I/O required
Single I/O gateway for cluster computer saturates
Does not scale with the size of the cluster

## Slide 16: What is Parallel I/O for Cluster Computers
Some or all of the cluster computers can be used for parallel I/O
Notes: Cluster is a collection of computers interconnected by a Local Area Network. The interconnection network can be Ethernet or high throughput and low latency network such as Myrinet or Infiniband. Typically specialized networks with low latencies are dedicated for High Performance Computing. The computers of the cluster are used for parallel computation. Some or all of them can be also used for providing Parallel I/O resources to the cluster.

## Slide 17: Objectives of parallel I/O
Resistance to multiple access
Scalability
High level of parallelism and load balance
Notes: Scalable resistance to the concurrent access by multiple compute nodes
Scalability as the number of I/O nodes increases
High level of parallelism and load balance for all application patterns and all types of I/O requests (small, large, continuous or fragmented)

## Slide 18: Concurrent Access by Multiple Compute Nodes
Parallel I/O Subsystem
No concurrent access overheads
No performance degradation
When the number of compute nodes increases
Notes: Concerning the concurrent access: there should be no overhead when the number of compute nodes simultaneously accessing the parallel I/O subsystem is increasing. In this case, the parallel I/O performance must decrease inverse-proportionally to the number of the concurrently accessing compute nodes.

## Slide 19: Scalable throughput of the parallel I/O subsystem
The overall parallel I/O throughput should increase linearly as the number of I/O nodes increases
Parallel I/O Subsystem
Number of I/O Nodes
Throughput
Notes: As for the scalability: the overall throughput of the parallel I/O subsystem should increase nearly linearly as the number of the I/O nodes in the subsystem increases

## Slide 20: Concurrency and Scalability = Scalable All-to-All Communication
Concurrency and Scalability (as the number of I/O nodes increases) can be represented by scalable overall throughput when the number of compute and I/O nodes increases
Number of I/O and Compute Nodes
All-to-All Throughput
I/O Nodes
Compute Nodes
Notes: The concurrency and the scalability objectives, can be represented by a single stress objective of having a scalable overall throughput as the number of compute and I/O nodes simultaneously increases

## Slide 21: How parallelism is achieved?
Split the logical file into stripes
Distribute the stripes cyclically across the subfiles
Subfiles
file1
file2
file3
file4
file5
file6
Logical file
Notes: After discussing the objectives let us have a look, how parallelism is achieved:
The parallelism is achieved by
splitting the global logical file into equally-sized stripes and by
cyclically distributing the stripes across a given number of subfiles

## Slide 22: Impact of the stripe unit size on the load balance
When the stripe unit size is large there is no guarantee that an I/O request will be well parallelized
subfiles
Logical file
I/O Request
Notes: The stripe unit size has an important impact on the load balance and the level of the achieved parallelism.
When the stripe unit size is large there is no guarantee that an I/O request will be well parallelized.

## Slide 23: Fine granularity striping with good load balance
Low granularity ensures good load balance and high level of parallelism
But results in high network communication and disk access cost
subfiles
Logical file
I/O Request
Notes: When the striping units are small the probability that an arbitrary I/O request will be well parallelized and distributed across the I/O nodes increases.

## Slide 24: Fine granularity striping is to be maintained
Most of the HPC parallel I/O solutions are optimized only for large I/O blocks (order of Megabytes)
But we focus on maintaining fine granularity
The problem of the network communication and disk access are addressed by dedicated optimizations
Notes: Most of the High Performance Computing (HPC) parallel I/O solutions are optimized for large I/O blocks (order of Megabytes)
In our development we are focused on maintaining fine granularity and small stripe unit sizes
The problem of the network communication and disk access overheads are solved not at the cost of the large stripe units but by developing dedicated optimizations

## Slide 25: Overview of the implemented optimizations
Disk access requests aggregation (sorting, cleaning-overlaps and merging)
Network communication aggregation
Zero-copy streaming between network and fragmented memory patterns (MPI derived datatypes)
Support of the multi-block interface efficiently optimizes application related file and memory fragmentations (MPI-I/O)
Overlapping of network communication with disk access in time (at the moment write operation only)
Notes: By supporting multi-block interface we permit optimization of application related fragmentations of both in memory and in global file.
For example MPI-I/O provides interface for specifying at the application the memory and file fragmentation patterns.
Multi-block interface permits an efficient integration of SFIO with applications having fragmented data patterns.
Disk access aggregation is carried out by analyzing the I/O requests at the level of subfiles, by sorting them according their offsets, by removing overlapped portions and by merging the fragmented requests into continuous requests.
Network communication aggregation for each pair of communicating nodes combines all small transfers into large chunks.
Zero-copy implementation streams the data directly between network and fragmented memory layouts without invoking memory copy operations.
It relies on MPI derived datatypes pointing on the fragmented layout of the memory.
Derived datatypes created by our library on the fly.
True zero-copy implementation relies on DMA access.
Network interface hardware communicates with the user memory space bypassing the traditional security copies via the system memory space.

## Slide 26: Disk access optimizations
Multi-block I/O request
Sorting
Cleaning the overlaps
Merging
Input: striped user I/O requests
Output: optimized set of I/O requests
No data copy
block 1
bk. 2
block 3
access1
access2
Local subfile
6 I/O access requests are merged into 2
Notes: Disk access optimization sub-layer is implemented at the compute nodes
The compute node caches all I/O requests related to single or multi block operation
The disk access optimization procedures are carried out on the level of requests and no data is copied
The requests are cached according to the I/O nodes
The optimization system sorts the cached requests, removes the overlapping segments and merges the requests into single requests
Thus an input set of I/O requests is converted into an optimal output set of merged I/O requests

## Slide 27: Network Communication Aggregation without Copying
Striping across 2 subfiles
Derived datatypes on the fly
Contiguous streaming
Logical file
From: application memory
Remote I/O node 1
Remote I/O node 2
To: remote I/O nodes
Notes: Merging of I/O requests still results in a requirement of communication between highly fragmented memory layout and the network
The fragmentation of the memory layout occurs due to two factors: the striping and the fragmentation dictated by the application patter itself
First, the communication is obviously carried out in large chunks instead of carrying individual transmission for each contiguous memory block
Secondly, there are no copies from the fragmented memory layout into contiguous memory block before transmission
We rely on MPI derided datatypes for streaming directly between the memory and network
The derived datatypes pointing on the fragmented memory layouts are created on the fly
Thus we avoid extra memory usage and copy operations
MPI implementation is typically extremely well optimized for a specific network interface, operating system and memory access architecture

## Slide 28: Optimized throughput as a function of the stripe unit size
3 I/O nodes
1 compute node
Global file size: 660 Mbytes
TNET
About 10 MB/s per disk
Notes: This chart shows the speedup achieved by the optimization system for small stripe unit sizes.
You can see that without fine-granularity-targeted optimizations the I/O throughput is optimal only when the striping factor is above 50KB.
This is the reason why most of the I/O systems are optimized for block sizes of a factor of Megabytes.
Our fine-granularity-targeted optimizations permit us to reach the optimal throughput at stripe unit sizes as low as 100 or 200 bytes.
50kB implies 1MB block size for good performance

## Slide 29: All-to-all stress test on Swiss-Tx cluster supercomputer
Stress test is carried out on Swiss-Tx machine
8 full crossbar 12-port TNet switches
64 processors
Link throughput is about 86 MB/s
Swiss-Tx supercomputer in June 2001
Notes: As I have shown in my previous slides, a stress test of a parallel I/O is to examine how the overall throughput scales when we increase at the same time the number I/O nodes and the number of concurrently accessing compute nodes. This stress test is carried out on the Swiss-T1 machine. The Swiss-T1 machine consists of 32 nodes, each comprising 2 processors. We dedicate one of the node’s processors for I/O and the second one for computing. With this assumption, when we increase the number of allocated nodes by an application, we increase the number of I/O and compute processors identically. Measurement of the overall I/O throughput of the application as a function of the number of allocated nodes permits us to evaluate the scalability of the parallel I/O library.

## Slide 30: All-to-all stress test on Swiss-Tx cluster supercomputer
Stress test is carried out on Swiss-Tx machine
8 full crossbar 12-port TNet switches
64 processors
Link throughput is about 86 MB/s
Notes: As I have shown in my previous slides, a stress test of a parallel I/O is to examine how the overall throughput scales when we increase at the same time the number I/O nodes and the number of concurrently accessing compute nodes. This stress test is carried out on the Swiss-T1 machine. The Swiss-T1 machine consists of 32 nodes, each comprising 2 processors. We dedicate one of the node’s processors for I/O and the second one for computing. With this assumption, when we increase the number of allocated nodes by an application, we increase the number of I/O and compute processors identically. Measurement of the overall I/O throughput of the application as a function of the number of allocated nodes permits us to evaluate the scalability of the parallel I/O library.

## Slide 31: SFIO on the Swiss-Tx cluster supercomputer
MPI-FCI
Global file size: up to 32 GB
Mean of 53 measurements for each number of nodes
Nearly linear scaling with 200 bytes stripe unit !
Network is a bottleneck above 19 nodes
Notes: This chart shows the overall I/O throughput of the application when increasing simultaneously both the number of I/O and concurrently accessing compute nodes.
Write throughput is higher since the I/O access and network communication operations are overlapped in time.
Global file size increases up to 32 GB as the number of allocated nodes increases.
This avoids super-linear performance due to the caching effect of the operating system.
53 measurements are carried out for each number of allocated nodes and the mean and maximal values are presented.
The stripe unit size us as low as 200 bytes.
The I/O system exhibits linear performance for up to 12 nodes.
Many I/O systems optimized for large blocks (order of Megabytes) are far below the linear performance and saturate quickly as the number of concurrently accessing compute nodes increases.
For 200 byte stripe unit sizes the linear scalability is remarkable.
The throughput of our parallel I/O library competes with the throughput of hardware parallel I/O solutions based on Storage Area Networks (SAN).
The throughput continues to increases but at a lower rate when the number of allocated nodes exceeds 12.
The analysis of the network topology has shown that the lower rate of the throughput increase is due to the fact that network plays the role of the bottleneck.
The gap between the maximum and the average throughputs is also increasing.
This is due to different allocation schemes of the nodes and correspondingly different underlying network topologies.

## Slide 32: Liquid scheduling for low-latency circuit-switched networks
Reaching liquid throughput in HPC wormhole switching and in Optical lightpath routing networks

## Slide 33: Upper limit of the network capacity
Given is a set of parallel transmissions
and a routing scheme
The upper limit of network’s aggregate capacity is its liquid throughput
Notes: The upper limit of the network

## Slide 34: Distinction: Packet Switching versus Circuit Switching
Packet switching is replacing circuit switching since 1970 (more flexible, manageable, scalable)

## Slide 35: Distinction: Packet Switching versus Circuit Switching
New circuit switching networks are emerging
In HPC, wormhole routing aims at extremely low latency
In optical network packet switching is not possible due to lack of technology

## Slide 36: Coarse-Grained Networks
In circuit switching the large messages are transmitted entirely (coarse-grained switching)
Low latency
The sink starts receiving the message as soon as the sender starts transmission
Message Sink
Message Source
Fine-Grained Packet switching
Coarse-grained Circuit switching

## Slide 37: Parallel transmissions in coarse-grained networks
When the nodes transmit in parallel across a coarse-grained network in uncoordinated fashion congestion may occur
The resulting throughput can be far below the expected liquid throughput

## Slide 38: Congestions and blocked paths in wormhole routing
When the message encounters a busy outgoing port it waits
The previous portion of the path remains occupied
Source1
Sink2
Sink1
Source2
Sink3
Source3

## Slide 39: Hardware solution in Virtual Cut-Through routing
In VCT when the port is busy
The switch buffers the entire message
Much more expensive hardware than in wormhole switching
Source1
Sink2
Sink1
Source2
Sink3
Source3
buffering

## Slide 40: Application level coordinated liquid scheduling
Hardware solutions are expensive
Liquid scheduling is a software solution
Implemented at the application level
No investments in network hardware
Coordination between the edge nodes and knowledge of the network topology is required

## Slide 41: Example of a simple traffic pattern
5 sending nodes (above)
5 receiving nodes (below)
2 switches
12 links of equal capacity
Traffic consist of 25 transfers

## Slide 42: Round robin schedule of all-to-all traffic pattern
First, all nodes simultaneously send the message to the node in front
Then, simultaneously, to the next node
etc

## Slide 43: Throughput of round-robin schedule
3rd and 4th phases require each two timeframes
7 timeframes are needed in total
Link throughput = 1Gbps
Overall throughput = 25/7x1Gbps = 3.57Gbps

## Slide 44: A liquid schedule and its throughput
6 timeframes of non-congesting transfers
Overall throughput = 25/6x1Gbps = 4.16Gbps

## Slide 45: Optimization by first retrieving the teams of the skeleton
Speedup: by skeleton optimization
Reducing the search space 9.5 times

## Slide 46: Liquid schedule construction speed with our algorithm
360 traffic patterns across Swiss-Tx network
Up to 32 nodes
Up to 1024 transfers
Comparison of our optimized construction algorithm with MILP method (optimized for discrete optimization problems)

## Slide 47: Carrying real traffic patterns according to liquid schedules
Swiss-Tx supercomputer cluster network is used for testing aggregate throughputs
Traffic patterns are carried out according liquid schedules
Compare with topology-unaware round robin or random schedules

## Slide 48: Theoretical liquid and round-robin throughputs of 362 traffic samples
362 traffic samples across Swiss-Tx network
Up to 32 nodes
Traffic carried out according to round robin schedule reaches only 1/2 of the potential network capacity

## Slide 49: Throughput of traffic carried out according liquid schedules
Traffic carried out according to liquid schedule practically reaches the theoretical throughput

## Slide 50: Liquid scheduling conclusions: application, optimization, speedup
Liquid scheduling: relies on network topology and reaches the theoretical liquid throughput of the HPC network
Liquid schedules can be constructed in less than 0.1 sec for traffic patterns with 1000 transmissions (about 100 nodes)
Future work: dynamic traffic patterns and application in OBS

## Slide 51: Fault-tolerant streaming with Capillary-routing
Path diversity and Forward Error Correction codes at the packet level
Notes: Hello everybody. My name is Emin Gabrielyan and my talk is about multi-path routing solutions for real-time streaming applications using Forward Error Corrections. This is a joint work between Swiss Federal Institute of Technology (EPFL) and Switzernet, a VoIP company in Switzerland

## Slide 52: Structure of my talk
The advantages of packet level FEC in Off-line streaming
Solving the difficulties of Real-time streaming by multi-path routing
Generating multi-path routing patterns of various path diversity
Level of the path diversity and the efficiency of the routing pattern for real-time streaming
Notes: First I will talk about the advantages of the packet level FEC codes (Forward Error Correction codes) in off-line streaming. Then I’ll present the difficulties arising in real-time streaming. I’ll show how multi-path routing solves these difficulties of real-time streaming. I’ll present an algorithm for building different multi-path routing patterns of increasing diversity. Finally I’ll present the relation between the diversity strength of the multi-path routing and the advantageousness of the routing for real-time streaming.

## Slide 53: Decoding a file with Digital Fountain Codes
A file is divided into packets
Digital fountain code generates numerous checksum packets
Sufficient quantity of any checksum packets recovers the file
Like when filling your cup only collecting a sufficient amount of drops matters
…
…
…
Notes: These checksum packets have a very interesting property. It is sufficient to collect a given number of those packets in order to be able to recover the original file (using a decoding algorithm). It does not matter which particular checksum packets are collected, only their quantity matters. Like with a water fountain, you need to feel your cup and you do not care about the choice of the drops.

## Slide 54: Transmitting large files without feedback across lossy networks using digital fountain codes
Sender transmits the checksum packets instead of the source packets
Interruptions cause no problems
The file is recovered once a sufficient number of packets is delivered
FEC in off-line streaming relies on time stretching
Notes: The satellite can transmit continuously different checksum packets of the original file encoded on-the-fly according to a digital fountain code. Now interruptions are not important. Only a sufficient quantity of any of the checksum packets is required to collect. If reception is interrupted the missing quantity can be collected later. A satellite can keep generating and transmitting the checksum packets during a long period of time (let’s say during 10 days) and with a high probability a car can collect the sufficient number of packets to decode the original file. Not only one car, but hundreds of thousands of independent cars can simultaneously receive a large file. Honda is planning to integrate Raptor codes into digital radio in order to broadcast to its vehicles large files, such as updates of GPS maps.

## Slide 55: In Real-time streaming the receiver play-back buffering time is limited
While in off-line streaming the data can be hold in the receiver buffer …
In real-time streaming the receiver is not permitted to keep data too long in the playback buffer
Notes: However, in real-time streaming, the receiver is not permitted to hold information in its buffer too long. The information must be delivered to the user in time. For example in VoIP the round trip time cannot exceed 600 milliseconds.

## Slide 56: Long failures on a single path route
If the failures are short, by transmitting a large number of FEC packets, receiver may constantly have in time a sufficient number of checksum packets
If the failure lasts longer than the playback buffering limit, no FEC can protect the real-time communication
Notes: In real-time streaming, in case of losses, the checksum packets for recovering the losses must arrive quickly, before expiration of the buffering time limit at the receiver (playback buffer time). A large amount of transmitted FEC packets may constantly provide in time a sufficient number of checksum packets at the receiver. However, if a total failure last longer the permitted playback buffer time, even infinite amount of FEC checksum packets cannot deliver the information in time. FEC can be useful only if the failures last no longer than the buffering time limit at the receiver.

## Slide 57: Applicability of FEC in Real-Time streaming by using path diversity
Reliable Off-line streaming
Reliable real-Time streaming
Time stretching
Playback buffer limit
Real-time streaming
Losses can be recovered by extra packets:
received later (in off-line streaming)
received via another path (in real-time streaming)
Path diversity replaces time-stretching
Path diversity
Notes: However, if in off-line streaming the lost packets can be compensated by other packets received at another period of time, in real-time streaming they can be compensated by other packets received at the same period of time but through another communication path. Therefore the path-diversity – a method orthogonal to time diversity – can make FEC applicable also for real-time streaming.

## Slide 58: Creating an axis of multi-path patterns
Intuitively we imagine the path diversity axis as shown
High diversity decreases the impact of individual link failures, but uses much more links, increasing the overall failure probability
We must study many multi-path routings patterns of different diversity in order to answer this question
Single path routing
Multi-path routing
Multi-path routing
Multi-path routing
Path diversity
Notes: Intuitively the path diversity ax must look like this. It is clear that for real-time streaming any multi-path routing is better than the single path routing. However, within multi-path routing solutions, we do not know if additional increase of diversity is beneficiary or not. Is not it sufficient for example to have only double path routing? Higher diversity minimizes the impact of individual link failures but from another side it requires a larger number of links to be used. Considering that each link has a failure probability, by using more links the overall rate of possible failures influencing the communication increases. Strong diversity may increase the FEC encoding effort of the sender, instead of decreasing. To address this question, we must study numerous multi-path routing patterns of increasing path diversity. The single path routing can be removed from our study.

## Slide 59: Capillary routing creates solutions with different level of path diversity
As a method for obtaining multi-path routing patterns of various path diversity we relay on capillary routing algorithm
For any given network and pair of nodes capillary routing produces layer by layer routing patterns of increasing path diversity
Path diversity
= Layer of Capillary Routing
Notes: In order to generate different routing patterns of increasing path diversity we use an algorithm – called capillary routing algorithm. For a given source and destination this algorithm can propose various multi-path routing patterns of increasing path diversity.

## Slide 60: Capillary routing – first layer
Reduce the maximal load of all links
First take the shortest path flow and minimize the maximal load of all links
This will split the flow over a few parallel routes
Notes: We use a linear programming (LP) method for constructing the capillary routing. At the first layer the objective of the linear program is to minimize the maximal load of all links. The solution of such a program distributes the flow across a few parallel paths.

## Slide 61: Capillary routing – second layer
Then identify the bottleneck links of the first layer
And minimize the flow of the remaining links
Continue similarly, until the full routing pattern is discovered layer by layer
Reduce the load of the remaining links
Notes: At the second layer we identify the bottleneck links of the multi-path route found in the first layer. The with a new objective we minimize the maximal load of all links, except the bottleneck links of the first layer. This leads us to a additional spreading of the route, whenever it was possible.

## Slide 62: Capillary Routing Layers
Single network [1]
4 routing patterns
Increasing path diversity

## Slide 63: Application model: evaluating the efficiency of path diversity
To evaluate the efficiencies of patterns with different path diversities we rely on an application model where:
The sender uses a constant amount of FEC checksum packets to combat weak losses and
The sender dynamically increases the number of FEC packets in case of serious failures
source packets
redundant packets
FEC block
Notes: With such a model we can compute how much of FEC checksum packets (or in other words redundant packets) must be injected by the sender into the stream of original packets in order to tolerate a desired packet loss rate t. For example in order to tolerate 10% packet losses the sender may need to add 20% redundant packets. This relation can be computed taking into account the type of the used code.

## Slide 64: Strong FEC codes are used in case of serious failures
Packet Loss Rate = 3%
Packet Loss Rate = 30%
When the packet loss rate observed at the receiver is below the tolerable limit, the sender transmits at its usual rate
But when the packet loss rate exceeds the tolerable limit, the sender adaptively increases the FEC block size by adding more redundant packets
Notes: When the packet loss rate reported by receiver is below the tolerable limit, the sender continues transmitting at the default mode. When the packet loss rate exceeds the tolerable limit, the sender computes how much redundant packets is necessary to combat the new losses and streams the media with the required number of redundant packets.

## Slide 65: Redundancy Overall Requirement
The overall amount of dynamically transmitted redundant packets during the whole communication time is proportional:
to the duration of communication and the usual transmission rate
to a single link failure frequency and its average duration
and to a coefficient characterizing the given multi-path routing pattern (analytical equation)
Notes: The overall number of redundant packets that the sender will need to transmit during the communication time is proportional (1) to the duration of the communication, (2) to the estimated frequency and duration of single link failures and (3) to a coefficient depending only on the chosen multi-path routing. Smaller this coefficient, better the multi-path routing is.

## Slide 66: ROR as a function of diversity
0
5
10
15
20
25
30
35
40
45
50
55
60
layer1
layer2
layer3
layer4
layer5
layer6
layer7
layer8
layer9
layer10
capillarization
Average ROR rating
Here is ROR as a function of the capillarization level
It is an average function over 25 different network samples (obtained from MANET)
The constant tolerance of the streaming is 5.1%
Here is ROR function for a stream with a static tolerance of 4.5%
Here are ROR functions for static tolerances from 3.3% to 7.5%
3.3%
3.9%
4.5%
5.1%
7.5%
6.3%
Notes: Here is ROR coefficient as a function of the capillary routing layer. We see that the capillarization of up to the 10th layer is advantageose as the ROR coefficient of the routing continues to decrease. The 5.1% at the side of the curve indicates the default constant tolerance of the streaming to the losses. The next example (the second curve) is for the streaming with the default static tolerance to 4.5% of packet losses. The curve is different, but the path diversity is beneficiary as well. Examples with other streaming parameters (all the remaining curves) show that even the strong path diversity with many underlying links always remains beneficiary.

## Slide 67: ROR rating over 200 network samples
ROR coefficients for 200 network samples
Each section is the average for 25 network samples
Network samples are obtained from random walk MANET
Path diversity obtained by capillary routing reduces the overall amount of FEC packets
Notes: Here is an example for many other network samples. This chart represents average curves for 200 network samples. It shows that the path diversity in typical network conditions is beneficiary. It is not only important the conversion of a single path routing to a simple multi-path routing. We show that in real-time streaming, with an additional development of the path diversity we may achieve a new significant gain in the number of redundant packets that the sender needs to transmit for protecting the communication.

## Slide 68: Conclusions
Although strong path diversity increases the overall failure rate,
Combined with erasure resilient codes
High diversity of main paths
and sub-paths is beneficiary for real-time streaming (except a few pathological cases)
With multi-path routing patterns real-time applications can have great advantages from application of FEC
Future work: using overly network to achieve a multi-path communication flow for VOIP over public Internet
Considering coding also inside network, not only at the edges for energy saving in MANET
Notes: Except a few pathological cases in typical network environment strong path diversity is beneficiary for real-time streaming. Capillary routing patterns significantly reduce the overall number of redundant packets required from the sender. Today’s commercial real-time streaming applications do not rely on packet level FEC, since with single path routing FEC is helpless. With multi-path routing patterns real-time applications can have great advantages from application of FEC. When the underlying routing cannot be changed, for example in public Internet, rely computers of an overly network can be used to achieve a multi-path communication flow. This is the end of my talk.

## Slide 69: Thank you!
Publications related to parallel I/O
[Gennart99] Benoit A. Gennart, Emin Gabrielyan, Roger D. Hersch, “Parallel File Striping on the Swiss-Tx Architecture”, EPFL Supercomputing Review 11, November 1999, pp. 15-22
[Gabrielyan00G] Emin Gabrielyan, “SFIO, Parallel File Striping for MPI-I/O”, EPFL Supercomputing Review 12, November 2000, pp. 17-21
[Gabrielyan01B] Emin Gabrielyan, Roger D. Hersch, “SFIO a striped file I/O library for MPI”, Large Scale Storage in the Web, 18th IEEE Symposium on Mass Storage Systems and Technologies, 17-20 April 2001, pp. 135-144
[Gabrielyan01C] Emin Gabrielyan, “Isolated MPI-I/O for any MPI-1”, 5th Workshop on Distributed Supercomputing: Scalable Cluster Software, Sheraton Hyannis, Cape Cod, Hyannis Massachusetts, USA, 23-24 May 2001
Conference papers on liquid scheduling problem
[Gabrielyan03] Emin Gabrielyan, Roger D. Hersch, “Network Topology Aware Scheduling of Collective Communications”, ICT’03 - 10th International Conference on Telecommunications, Tahiti, French Polynesia, 23 February - 1 March 2003, pp. 1051-1058
[Gabrielyan04A] Emin Gabrielyan, Roger D. Hersch, “Liquid Schedule Searching Strategies for the Optimization of Collective Network Communications”, 18th International Multi-Conference in Computer Science & Computer Engineering, Las Vegas, USA, 21-24 June 2004, CSREA Press, vol. 2, pp. 834-848
[Gabrielyan04B] Emin Gabrielyan, Roger D. Hersch, “Efficient Liquid Schedule Search Strategies for Collective Communications”, ICON’04 - 12th IEEE International Conference on Networks, Hilton, Singapore, 16-19 November 2004, vol. 2, pp 760-766
Papers related to capillary routing
[Gabrielyan06A] Emin Gabrielyan, “Fault-tolerant multi-path routing for real-time streaming with erasure resilient codes”, ICWN’06 - International Conference on Wireless Networks, Monte Carlo Resort, Las Vegas, Nevada, USA, 26-29 June 2006, pp. 341-346
[Gabrielyan06B] Emin Gabrielyan, Roger D. Hersch, “Rating of Routing by Redundancy Overall Need”, ITST’06 - 6th International Conference on Telecommunications, June 21-23, 2006, Chengdu, China, pp. 786-789
[Gabrielyan06C] Emin Gabrielyan, “Fault-Tolerant Streaming with FEC through Capillary Multi-Path Routing”, ICCCAS’06 - International Conference on Communications, Circuits and Systems, Guilin, China, 25-28 June 2006, vol. 3, pp. 1497-1501
[Gabrielyan06D] Emin Gabrielyan, Roger D. Hersch, “Reducing the Requirement in FEC Codes via Capillary Routing”, ICIS-COMSAR’06 - 5th IEEE/ACIS International Conference on Computer and Information Science, 10-12 July 2006, pp. 75-82
[Gabrielyan06E] Emin Gabrielyan, “Reliable Multi-Path Routing Schemes for Real-Time Streaming”, ICDT06, International Conference on Digital Telecommunications, August 29 - 31, 2006, Cap Esterel, Côte d’Azur, France